GEARBOX

The Tamiya twin-motor gearbox is a small (3-inch long) plastic gearbox. It contains two small DC motors that drive separate 3mm hexagonal output shafts. There are two ways to put the kit together: with a high-speed 58:1 gear ratio or with a slower 203:1 gear ratio. Either way, the motors provide plenty of power to drive any small robot. For a gearbox with a similar form factor and more gear ratio options, see the Tamiya double gearbox.

### General specifications

| Typical operating voltage: | 3 V |
| --- | --- |
| Gear ratio options: | 58:1 and 204:1 |
| Free-run motor shaft speed @ 3V: | 12300 rpm1 |
| Free-run current @ 3V: | 150 mA2 |
| Stall current @ 3V: | 2100 mA |
| Motor shaft stall torque @ 3V: | 0.5 oz·in3 |
| Color: | gray |

### Notes:

1

A theoretical speed of the gearbox output shaft can be computed by dividing this speed by the gear ratio.

2

This is the no-load current of the motor when disconnected from the gears in the gearbox; the no-load current of the entire gearbox with the motor connected will be slightly higher and will vary depending on the gear ratio.

3

A theoretical torque of the gearbox output shaft can be computed by multiplying this torque by the gear ratio.

### File downloads

Mabuchi motor FA-130 datasheet (see model #18100) (58k pdf)